## Slide 1: CISSP Guide to Security Essentials, Second Edition
Chapter 10
Telecommunications and Network Security
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 2: Objectives
Wireline and wireless telecommunication technologies
Wired and wireless network technologies
Network topologies and cabling
The OSI and TCP/IP network models
TCP/IP networks, protocols, addressing, devices, routing, authentication, access control, tunneling, and services
Network based threats, attacks, vulnerabilities, and countermeasures
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 3: Wired Telecom Technologies
DS-1, aka T-1
  24 voice or data channels, each 1.544 Mbit/sec
Other T-carrier protocols
  DS-3 (673 voice channels, 45mBit/s)
  DS-4 (4,032 channels, 274mBit/s)
  DS-5 (5,760 channels, 400mBit/s)
E-1 – Euro version
  32 channels instead of 24, otherwise similar
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: DS-1 created by Bell Labs. (used in US, Korea, Japan)
a DS-1 carries 24 voice channels (each called a DS-0) at 64 kbit/s each. When used to carry data traffic, a DS-1 can be divided into 24 data channels at 64 kbit/s each, into a smaller number of faster channels, or a single data channel at 1.544 Mbit/s.
E-1 p.377 with Tables.

## Slide 4: Wired Telecom Technologies (cont.)
SONET (Synchronous Optical NETwork)
  High speed, fiber optic, encapsulates T-protocols, ATM, TCP/IP
  OC-1 - 48.960 Mbit/sec
  OC-3 - 150.336 Mbit/sec
  OC-12 - 601.344 Mbit/sec
  OC-24 - 1,202.688 Mbit/sec
  OC-48 - 2,405.376 Mbit/sec
  OC-96 - 4,810.752Mbit/sec
  OC-192 - 9,621.504 Mbit/sec
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Synchronous optical networking (SONET) is the prevalent standard in North America for transporting voice and data over optical fiber. SONET is a physical-layer tech- nology that can be used to encapsulate network technologies such as ATM, MPLS, and TCP/IP. SONET is also used to encapsulate slower DS-1 type technologies.
Higher SONET rates are in development including OC-3072, whose rate is 160 Gbit/s.

## Slide 5: Wired Telecom Technologies (cont.)
MPLS (Multiprotocol Label Switching)
  Packet switched technology, encapsulates TCP/IP, ATM, SONET, Ethernet frames) over WANs.
  Carries voice + data, has QoS (quality of service) capabilities to guarantee jitter-free voice and other media such as video
  Replacing Frame Relay and ATM
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 6: Wired Telecom Technologies (cont.)
DSL (Digital Subscriber Line)
  Digital packet over copper voice circuits at higher clock rate, coexists with low frequency voice
  Modem used on subscriber side to convert DSL signals to Ethernet (and sometimes Wi-Fi)
  DSLAM (Digital Subscriber Line Access Multiplexer) on telco end aggregates signals
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Small filters are used to block the high frequencies from the data signal from interfering with telephones that are connected to the same wires.

## Slide 7: Wired Telecom Technologies (cont.)
ATM (Asynchronous Transfer Mode)
  Synchronous, connection-oriented packet protocol (packet-switching)
  Packets called cells, are fixed length (5 byte header, 48 byte payload)
  Intended to replace 10mB Ethernet, but it didn’t really catch on. 100mB and 1000mB Ethernet was favored instead, also giving way to MPLS.
  ATM is connection-oriented; before data is transmitted between nodes, an end-to-end virtual circuit is established.
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 8: Wired Telecom Technologies (cont.)
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 9: Wired Telecom Technologies (cont.)
Other wired telecom technologies
  Data Over Cable Service Interface Specification (DOCSIS)
  PSTN (Public Switched Telephone Network)
  Frame Relay
  ISDN (Integrated Services Digital Network)
  SDH (Synchronous Digital Hierarchy)
  X.25
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Data Over Cable Service Interface Specification (DOCSIS). This is the technology that facilitates Internet access over hybrid fibre coaxial (HFC) television networks through popular cable modems. Because a part of the HFC network is a shared medium, data between the service provider and the subscriber are encrypted. Service providers also employ MAC-layer security to prevent unauthorized parties from accessing the network. The maximum throughput is 128 kbit/s, which was soon overcome by DSL and DOCSIS and has contributed to the decline of ISDN.
Synchronous Digital Hierarchy (SDH). This is the prevalent standard for voice and data communications over fiber networks outside of North America. It is the functional equivalent of SONET, which is used in North America.
X.25. This is a packet-switched network that is transported over lease lines, ISDN, and regular phone lines. X.25 is considered a legacy technology, having been largely replaced by other technologies such as MPLS, DSL, ISDN, and frame relay.
Synchronous Digital Hierarchy (SDH). This is the prevalent standard for voice and data communications over fiber networks outside of North America. It is the functional equivalent of SONET, which is used in North America.
X.25. This is a packet-switched network that is transported over lease lines, ISDN, and regular phone lines. X.25 is considered a legacy technology, having been largely replaced by other technologies such as MPLS, DSL, ISDN, and frame relay.

## Slide 10: Wireless Telecom Technologies
CDMA2000 (code division multiple access)
  Data transport: 1XRTT (153 kbit/s), EVDO (2.4 Mbit/s), EVDV (3.1 Mbit/s)
GPRS (General Packet Radio Service)
  Encapsulated in GSM (Global System for Mobile communications) protocol (114kbit/s)
EDGE (Enhanced Data rates for GSM Evolution)
  Up to 1Mbit/s
LTE (Long Term Evolution)
  Up to 300 Mbit/s downlink, 75 Mbit/s uplink
UMTS (Universal Mobile Telecommunications System)
  Transported over WCDMA, up to 14Mbit/s)
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: 5G : up to 10Gb/s
CDMA2000 (code division multiple access) is a mobile radio technology used to transmit voice and data between subscriber devices (usually cellular phone handsets and PCMCIA cellular modems) and network providers’ base stations, for purposes of voice and data communications.
General Packet Radio Service (GPRS) is a data-centric mobile radio technology used in the Global System for Mobile Communications (GSM) network. GPRS devices include mobile handsets and PCMCIA-based modems for PCs.
Enhanced Data rates for GSM Evolution (EDGE) and Enhanced GPRS (EGPRS) are the successors to GPRS
(LTE) is a high-speed wireless data communication technology that is based on GSM and UMTS technologies.
(UMTS) is another data-centric mobile radio technology found in wireless handsets and PC card modems.

## Slide 11: Wireless Telecom Technologies (cont.)
WiMAX (Worldwide Interoperability for Microwave Access)
  Based on IEEE 802.16, WiMAX is a wireless competitor to DSL and cable modems, also competes with CDMA, GPRS, EDGE, UMTS
  Rates range from 2 to 12 Mbit/s, theoretically as high as 70 Mbit/s
CDPD (Cellular Digital Packet Data) – first data over cellular, used AMPS analog carrier, up to 19.2 kbit/s
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Last-Mile technology. Another advantages of WiMAX, is a relatively new technology that enables communication over a maximum distance of 30 miles – compared to 300 feet for WiFi. Of course, the longer the distance, the slower the speed, but it is still faster and has a longer range than WiFi. Ideally, speeds of around 10 MBps could be achieved with a range of 1 – 6 miles
Like other wireless technologies, WiMAX is a shared medium, meaning that more simultaneous users means lower effective throughput.

## Slide 12: Wired Network Technologies
Ethernet
  Frame-based protocol
    14 byte header
    Payload (46-1500 bytes)
    Checksum
    Inter-frame gap
  Error detection: Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
  MAC address: 6 bytes. Format xx.xx.xx.yy.yy.yy.
    xx.xx.xx assigned to manufacturer
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Header. The Ethernet header consists of 14 bytes that include: –
Preamble. This consists of 7 octets of 10101010.
Start of frame. This consists of 1 octet of 10101011.
6-byte destination MAC address.
6-byte source MAC address. –
2-byte Ethernet frame type.
Checksum. This is a 4-byte CRC (cyclic redundancy check) that is used to verify the integrity of the entire frame.
Interframe gap. After the frame is transmitted, the sending station pauses for 960 ns before sending the next frame.
The first three bytes of a MAC address are known as the Organizationally Unique Identifier (OUI), which identifies the organization that manufactured the device. The last three bytes are assigned by the device’s manufacturer and must be unique.

## Slide 13: Wired Network Technologies (cont.)
Ethernet devices
  Hub – connects local stations together; broadcast
  Repeater – extend signal over distances
  Switch – like a hub but does not broadcast
  Router – connect networks to each other
  Gateway – translates various types of communications
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Strictly speaking, a router is a type of gateway, but other types exist, including frame relay switches, ATM to IP switches, and so on.

## Slide 14: Wired Network Technologies (cont.)
Token ring
  Logical ring
  Speed: 4Mbit/s and 16Mbit/s
  Mostly replaced by Ethernet
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: A token ring network is a physical star. Each station on the network is connected to a Multi- station Access Unit by a cable.
A token ring network is a logical ring. Data transmission is facilitated by the use of a logical token; only the station in possession of the network’s token may transmit data. The token is passed from station to station; when a station has nothing to transmit, it merely passes the token to the next station. When a station does have data to transmit, it is attached to the token and passed along. When the token (with its payload) reaches the destination station, the payload is removed, and the destination station then passes an empty token along. Algorithms in the MAU handle situations such as a lost token, the introduction of a new node on the network, and network rebooting.

## Slide 15: Wired Network Technologies (cont.)
Universal Serial Bus (USB)
  Successor to RS-232 serial
  Speeds
    USB 1.0/1.1 – 1.5Mbits/s and 12Mbits/s
    USB 2.0 – 480Mbits/s
    USB 3.0 – 4.8Gbits/s
  Hot pluggable
  Used to connect peripheral and human interface devices
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: The USB standard includes the use of a five-port hub (one port that connects to the host computer and four open ports) that facilitates the connection of additional peripherals.

## Slide 16: Wired Network Technologies (cont.)
RS-232
  Serial communications, speeds 110bit/s – 57.7kbit/s
  Used to connect communications devices such as modems, and human interface devices such as mice
  Largely replaced by USB
HSSI (High Speed Serial Interface) – 52Mbits/s, cable length 50’, used to connect WAN devices
Fibre Channel – gigabit protocol used in SANs (Storage Area Networks)
FDDI (Fiber Distributed Data Interface) – token technology over fiber that has been replaced by gigabit Ethernet and SONET
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: The RS-232 standard accommodated many throughput speeds ranging from 110 bps to 115 kbps. Flow control has been implemented in several ways, including hardware signaling (through various additional connector pins) and software signaling (through the use of XON and XOFF (ASCII 0x11 and 0x13, respectively).
The computer end of an RS-232 connection is often called DCE (Data Circuit-terminating Equipment); the peripheral end is often called DTE (Data Terminal Equipment).

## Slide 17: Wired Network Technologies (cont.)
Network cabling
  Ethernet
    10BASE-T – this is the commonly twisted-pair network cable that supports the Category 3, 5, or 6 ANSI standard. This cable has 8 conductors, of which 4 are used. An 8-pin RJ45 connector is used to connect a cable to a device.
    100BASE-TX – the same twisted-pair network cable (Category 5 and 6) and connectors as 10BASE-T, and also uses just 4 of the 8 conductors.
    1000BASE-T – the same twisted-pair network cable and connectors as 100BASE-TX, except that all 8 conductors are used.
    10BASE2 – the old “thinnet” coaxial cabling with twist-lock BNC connectors – rarely used.
    10BASE5 – the old “thicknet” coaxial cabling that is rarely used.
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 18: Wired Network Technologies (cont.)
Twisted pair cabling
  Category 3 – consists of four twisted pairs in a single jacket. Suitable only for 10Mbit/s Ethernet. Superseded by Category 5 and 5e.
  Category 5 – consists of four twisted pairs in a single jacket. Maximum length is 100m. Suitable for 100Mbit/s and can be used for Gigabit Ethernet.
  Category 5e – supersedes Category 5 and includes specifications for far end crosstalk.
  Category 6 – backward compatible with Category 5 and 5e, but higher specifications for noise and crosstalk, making it more suitable for Gigabit Ethernet.
  Category 7 – even more stringent than Category 6 cabling, Cat-7 is suitable for 10Gbit/s networks.
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 19: Wired Network Technologies (cont.)
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 20: Wired Network Technologies (cont.)
Cabling (cont.)
  Optical
    Carries signal in the form of light instead of electricity
    Greater speeds and distances possible
    More expensive
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 21: Network Topologies
Bus. All of the nodes in the network are connected to a single conductor. A break in the network conductor will cause some or the entire network to stop functioning. Early Ethernet networks consisting of thinnet coaxial cabling were bus networks.
Ring. All of the nodes are connected to exactly two other nodes, forming a circular loop. Breaking any conductor will cause the network to stop functioning.
Star. All nodes are connected to a central device. A break in a conductor will disconnect only one node, and the remaining nodes will continue functioning. Ethernet networks are physical stars, with computers connected to central hubs or switches. Token ring networks, while logically as a ring, are physically wired as a star.
Mesh. Nodes connect to all other proximate nodes.
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 22: Network Topologies (cont.)
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 23: Wireless Network Technologies
Wi-Fi, also known as WLAN, Wireless LAN
  Wireless data link layer network protocol
  Bandwidth up to 248Mbit/s, distances to 100m
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 24: Wireless Network Technologies (cont.)
Standard | Spectrum | Data Rate | Range | Released
802.11a | 5 GHz | 54 Mbit/s | 120 m | 1999
802.11b | 2.4 GHz | 11 Mbit/s | 140 m | 1999
802.11g | 2.4 GHz | 54 Mbit/s | 140 m | 2003
802.11n | 2.4 / 5 GHz | 248 Mbit/s | 250 m | 2009
802.11y | 3.7 GHz | 54 Mbit/s | 5000 m | 2008
Wi-Fi standards
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 25: Wireless Network Technologies (cont.)
Wi-Fi security
  SSID should be a non-default value
  SSID broadcast should be disabled
  MAC access control
  Authentication
  Encryption
    WEP (Wired Equivalent Privacy)
    WPA (Wireless Protected Access)
    WPA2 (superset of WPA, full standard)
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: WiFi Protected Access (WPA), a protocol standard that is a replacement for WEP.
WPA is a subset of the IEEE 802.11i-2004 (WPA2) specification.
–WPA2 is the full IEEE 802.11i-2004 specification, a superset of WPA. Both WPA and WPA2 can operate in a PSK (pre-shared key) mode, where the encryption key is stored in the WiFi access point.
–WPA2 Enterprise is the WPA2 protocol when an external authentication source, such as RADIUS, is used.

## Slide 26: Wireless Network Technologies (cont.)
Bluetooth
  Personal Area Network (PAN) technology
  Data rate: 1Mbit/s – 3Mbit/s
  Distance: up to 10 m
  Devices can authenticate through a process called “pairing”, during which two devices can exchange a cryptographic secret key that the two devices can later use to securely identify themselves.
  Communications between paired devices can also be encrypted.
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 27: Wireless Network Technologies (cont.)
IrDA
  Infrared Data Association standard
  Infrared light spectrum from 2.4kbit/s to 16Mbit/s
    Requires line-of-sight
  Once popular, now replaced with Bluetooth
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 28: Wireless Network Technologies (cont.)
Wireless USB (WUSB)
  Wireless protocol designed for wireless connectivity of various computer peripherals
    Printers, digital cameras, hard disks, and other high-throughput devices
  Bandwidth ranges from 110 Mbit/s at 10 meters to 480 Mbit/s at 3 meters
  3.1 to 10.6 GHz frequency range
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 29: Wireless Network Technologies (cont.)
Near Field Communication (NFC)
  Ultra-short distance (up to 10cm or 4”)
  Rates: 106 kbit/s, 212 kbit/s, or 424 kbit/s
  Active or passive mode
    Passive mode ideal for key card access control
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: NFC can operate in passive mode and active mode. In passive mode, one device is acting as a transponder, not unlike an RF-powered key card. In active mode, both devices are actively communicating to one another.
NFC’s short range makes it ideal for use as a mobile wallet application where a mobile device such as a wallet card or cell phone can be used as a payment token for a merchant transaction or ticketing application.
p389

## Slide 30: OSI Network Model
Physical
Data link
Network
Transport
Session
Presentation
Application
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 31: OSI Network Model: Physical
Concerned with a network’s physical media
  Electrical
  Optical
  Radio frequency
Example standards
  RS-232, RS-422, T1, E1, 10Base-T, SONET, DSL, 802.11a (physical), Twinax
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 32: OSI Network Model: Data Link
Concerned with the transfer of data between nodes
Manages error correction for any errors that take place at the physical layer
Example standards
  802.3 (Ethernet), 802.11a MAC, GPRS, AppleTalk, ATM, FDDI, Fibre Channel, Frame Relay, PPP, SLIP, Token Ring, Wi-MAX
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 33: OSI Network Model: Network
Used to transport variable-length data sequences between nodes
Manages fragmentation and reassembly
Communications are point-to-point
No notion of a “connection”
Delivery of data not done here
Example standards
  IP, ICMP, ARP, IPX
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 34: OSI Network Model: Transport
Manages the delivery of data from node to node on a network
  Even when there are intermediate devices such as routers and a variety of physical media between the nodes
  Manages “connections”
    Guarantee the order of delivery of data packets, packet reassembly, error recovery
  Examples: UDP, TCP, IPsec, PPTP, L2TP, SPX
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 35: OSI Network Model: Session
Manages connections between nodes, including session establishment, communication, and teardown
Example standards
  NetBIOS, TCP, SIP
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 36: OSI Network Model: Presentation
Deals with the presentation or representation of data in a communications session
  Character set translation
  Compression
  Encryption
Examples of presentation-layer standards include SSL, TLS, MIME, and MPEG
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 37: OSI Network Model: Application
Top-most layer in the OSI network model
Concerned with the delivery of data to and from applications
Examples standards
  DNS, NFS, NTP, DHCP, SMTP, HTTP, SNMP, SSH, Telnet, WHOIS
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 38: TCP/IP Protocol Model
Link
Internet
Transport
Application
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 39: TCP/IP Protocol Model
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 40: TCP/IP Protocol Model: Link
Concerned with node to node delivery
Example standards
  Wi-Fi
  Ethernet
  Token Ring
  ATM
  Frame Relay
  PPP
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 41: TCP/IP Protocol Model: Internet
Also known as the Network layer
Concerned with end-to-end packet delivery, even through intermediate devices such as switches and routers
Protocols
  IPv4
  IPv6
  ARP
  RARP
  ICMP
  IGMP
  IPsec
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 42: TCP/IP Protocol Model: Internet (cont.)
Internet layer routing protocols
  RIP
  OSPF
  IS-IS
  BGP
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 43: TCP/IP Protocol Model: Internet (cont.)
Internet layer addressing
  Network addresses in IPv4 are 32 bits in length
    Expressed as a dot-decimal notation, xx.xx.xx.xx, where the range of each ‘xx’ is 0-255 decimal
    Typical network address is 141.204.13.200
  Subnets and subnet masking
    IP address divided into two parts: network and node
    Subnet mask used to distinguish network and node portions; e.g. 255.255.255.0
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 44: TCP/IP Protocol Model: Internet (cont.)
Internet layer addressing (cont.)
  Default gateway – node that connects to other networks
  Address allocation by Regional Internet Registry (RIR), ISPs
  Reserved address blocks
    Private networks
      10.0.0.0 – 10.255.255.255
      172.16.0.0 - 172.31.255.255
      192.168.0.0-192.168.255.255
    Loopback: 127.0.0.1 - 127.0.0.255 (127.0.0.1 = “me”)
    Multicast: 224.0.0.0-239.255.255.255
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 45: TCP/IP Protocol Model: Internet (cont.)
Internet layer addressing (cont.)
  Network address translation (NAT)
    Internal private addresses are translated into public routable addresses at the network boundary
  Classful networks
    Class A
    Class B
    Class C
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 46: TCP/IP Protocol Model: Internet (cont.)
Internet layer addressing (cont.)
  Classless networks (Classless Internet Domain Routing (CIDR))
    Variable length subnet masks, not limited to just Class A, B, C
  Types of addressing
    Unicast (regular node addresses)
    Broadcast (send to all nodes on a subnet)
    Multicast (send to a group of nodes on different networks)
    Anycast (send to only one of a group of nodes)
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 47: TCP/IP Protocol Model: Transport
TCP Protocol
  Connection oriented, persistent connections, dedicated and ephemeral ports, sequencing, flow control, guaranteed delivery
  Examples: FTP, HTTP, Telnet
UDP Protocol
  Connectionless, dedicated port numbers only, no sequencing, no guarantee of delivery
  Examples: DNS, TFTP, VoIP
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 48: TCP/IP Protocol Model: Application
Topmost layer in the TCP/IP protocol stack
Protocols: DHCP, DNS, Finger, FTP, HTTP, LDAP, NFS, NIS, NTP, Rlogin, RPC, Rsh, SIP, SMTP, SNMP, Telnet, TFTP, VoIP, Whois
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 49: TCP/IP Routing Protocols
Router-to-router communication protocol used by routers to help determine the most efficient network routes between two nodes on a network
Helps routers make good routing decisions (making the right choice about which way to forward packets)
RIP (Routing Information Protocol) – one of the early routing protocols
  Hop count the primary metric, maximum = 15
IGRP (Interior Gateway Routing Protocol) – Cisco proprietary
  Multiple metrics: hop count (max 255), bandwidth, delay, load, MTU, and reliability
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 50: TCP/IP Routing Protocols (cont.)
EIGRP (Enhanced Interior Gateway Routing Protocol) – Cisco proprietary
  Advances over IGRP including VLSM
OSPF (Open Shortest Path First) – Open standard for enterprise networks
  Metric is “path cost” (primarily hops and speed)
  Uses authentication to prevent route spoofing
BGP (Border Gateway Protocol) – the dominant Internet routing algorithm
IS-IS (Intermediate system to intermediate system) – used primarily by large ISP networks
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 51: Remote Access/Tunneling Protocols
Tunneling: encapsulating packets of one protocol within another
  Can include encryption
  Reasons: protection of encapsulated protocol; hide details of intermediary network, authentication of traffic
  Protocols
    VPN – generic term for tunneled (and usually encrypted) network connection from a public network to a private network
    SSL / TLS
    SSH
    IPsec
    Others: L2TP, PPP, PPTP, SLIP
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 52: Remote Access/Tunneling Protocols (cont.)
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 53: Authentication Protocols
RADIUS (Remote Authentication Dial In User Service)
  Over-the-wire protocol from client to AAA (authentication, authorization, accounting) server
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 54: Authentication Protocols (cont.)
Diameter – more advanced RADIUS replacement
TACACS (Terminal Access Controller Access-Control System) – authenticates user to a network.
  Between access point or gateway and an AAA server
802.1X – port level access control. Device authenticates before device will be able to communicate on the network.
NAC (Network Access Control) – an approach for controlling which devices may connect to a network – device must meet minimum standards like anti-virus, host intrusion prevention, etc.
CHAP (Challenge-Handshake Authentication Protocol)
  Between client system and gateway. Challenge/Response/Authenticate.
PPP uses CHAP
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: CHAP works by using a three-way handshake as follows:
1.Gateway sends a challenge message to the user system
2.User system responds with a value that is a hash of the challenge plus a shared secret that both the user and the gateway know
3.Gateway compares user system’s hashed value with its own; if they match, the connection is permitted; if they do not match, the connection is terminated

## Slide 55: Authentication Protocols (cont.)
EAP (Extensible Authentication Protocol)
  Authentication Framework – used to authenticate users in wired and wireless networks. Used by WPA and WPA2 wireless network standards.
PEAP (Protected Extensible Authentication Protocol)
  used in wireless networks to authenticate users
  PEAP uses an SSL/TLS tunnel to encrypt authentication information
PAP (Password Authentication Protocol) - unsecure because protocol is unencrypted
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Several EAP protocols exist, including:
EAP-PSK. This is a mutual authentication protocol using a Pre-Shared Key (PSK), usually to protect a network-based resource using a single password for all users.
EAP-IKEv2. This is authentication based upon the Internet Key Exchange (IKE). protocol
EAP-AKA. This is used for authentication in UMTS (Universal Mobile Telecommunications System), a mobile communications standard.
EAP-SIM. Used for authentication in GSM (Global System for Mobile Communications), a global standard for mobility devices such as cell phones and wireless broadband modems.
(PEAP) (and sometimes known as Protected EAP) is a protocol used in wireless networks to authenticate users. PEAP uses an SSL/ TLS tunnel to encrypt authentication information that is exchanged between the client and the authentication server or device. Tshere are two forms of PEAP:
PEAPv0. This is the most common form, usually known as just PEAP. PEAPv0 uses CHAP for authentication. PEAPv1. This form, not in common use, supports authentication using token cards and directories.
(PAP) is a simple authentication protocol used by PPP to authenticate users. PAP is considered unsecure because user credentials are passed unencrypted.

## Slide 56: Network Threats
The expressed potential for the occurrence of a harmful event such as an attack
  DoS / DDoS – designed to flood or cause malfunction
  Teardrop - attacker sends mangled packet fragments with overlapping and oversized payloads to a target system
  Sequence number – guesses upcoming sequence numbers as a method for disrupting communications (session hijacking)
  Smurf - large number of forged ICMP echo requests. The packets are sent to a target network’s broadcast address, which causes all systems on the network to respond
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 57: Network Threats (cont.)
Threats (cont.)
  Ping of Death – ICMP echo request, 64k length
  SYN flood – large volume of TCP SYN packets, consumes resources on target system
  Worm – automated, self-replicating program
  Spam – unsolicited commercial e-mail (UCE): fraud, malware, marketing
  Phishing – emails luring users to fraudulent sites
  Pharming – attack on DNS that re-directs access to legitimate sites to imposter sites
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 58: Network Vulnerabilities
Unnecessary open ports
Unpatched systems
Poor and outdated configurations
Default passwords
Exposed cabling
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Vulnerabilities are defined as weaknesses that make targets susceptible to attack, resulting in harm or compromise of sensitive information.

## Slide 59: Network Countermeasures
Access control lists
Firewalls
Intrusion Detection System (IDS)
  Network based (NIDS)
  Host based (HIDS)
Intrusion Prevention System (IPS)
  Network and host based
Data Leakage Prevention systems (DLP)
Protection of network cabling
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: Firewalls: Packet Filtering, Stateful, Application-layer filters (examine payloads for known malicious patterns/content).
DLP: Data LOSS Prevention systems: device that monitors networks, systems (or both) by detecting out-of-policy movement or storage of sensitive info. A DLP system can examine network traffic to detect the movement of sensitive information, or it can examine data stores to detect the presence of sensitive information.

## Slide 60: Network Countermeasures (cont.)
Anti-virus software
Private addressing (10.*.*.*, etc.)
Close unnecessary ports and services
Security patches
Unified Threat Management (UTM)
Gateways – filtering intermediaries
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.
Notes: (UTM) is a term used to describe a class of security devices and appliances that perform many functions in order to simplify the defenses in a network. A UTM system can contain one or more of the following:
Firewall/ IDS /IPS /Anti-virus /Anti-spam /World Wide Web content filtering /VPN remote access
A principle advantage of UTM is the consolidation of these important network-based security features in a single product. What is a disadvantage?
Single point of failure, loss of heterogeneity.

## Slide 61: Summary
Wired telecom technologies include DS-1 (T-1), SONET, Frame Relay, ATM, DSL, and MPLS.
Wireless telecom technologies include CDMA2000 (which includes 1xRTT and EVDO), GPRS, EDGE, LTE, UMTS, and WiMAX.
Wired network technologies include Ethernet, ATM, Token Ring, USB, RS-232.
Wireless network technologies include Wi-Fi, Wireless USB, NFC, and IrDA.
Ethernet is a frame technology that uses an 8-octet address.
The three network topologies are bus, ring, and star.
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 62: Summary (cont.)
Wi-Fi wireless networks can be secured by turning off SSID broadcast, using a non-default SSID, utilizing WPA or WPA2 encryption, using user based authentication, and MAC based access control .
The seven layers of OSI are: physical, data link, network, transport, session, presentation, and application.
The five-layer of TCP/IP are: physical, data link, network / internet, transport, and application.
Common tunneling (encapsulation) protocols are SSL, SSH, IPsec, L2TP, PPTP, and PPP.
Common authentication protocols are RADIUS, Diameter, CHAP, EAP, and PEAP. TACACS and PAP are no longer widely used.
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 63: Summary (cont.)
TCP/IP link layer protocols include Ethernet, Token Ring, ATM, Frame Relay, and PPP.
TCP/IP internet layer protocols include IPv4, IPv6, ARP, RARP, ICMP, IGMP, and Ipsec.
TCP/IP transport layer protocols include TCP and UDP.
TCP/IP application layer protocols include DHCP, DNS, FTP, HTTP, LDAP, NTP, RPC, SIP, SMTP, SNMP, TELNET, TFTP, and VoIP.
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 64: Summary (cont.)
Common network based attacks are Denial of Service (DoS), Distributed Denial of Service (DDoS), Teardrop, Sequence number, Smurf, Ping of Death, SYN flood, worms, spam, and phishing.
Common network based vulnerabilities are unneeded open ports, unpatched systems and devices, default passwords, and misconfigured systems and devices.
Effective countermeasures are access control lists (ACLs), firewalls, intrusion detection systems, intrusion prevention systems, private addressing, closing unnecessary ports and services, installing security patches, and using gateways. UTM (unified threat management) devices that perform many defensive functions are gaining use.
© 2016 Cengage Learning®. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.